## Slide 1: Introduction to Arduino
Rochester MakerSpace
2021
Notes: Welcome
Introductions

## Slide 2: Class Objectives
Become familiar with Arduino hardware and software
Be aware of the range of Arduino-supported boards and how to choose one for your project
Understand how to connect and operate Arduino hardware from a PC or Mac
Understand how to create and run a program on an Arduino
Understand how to control a simple circuit from an Arduino
Get a starter list of resources for learning more
Be excited by the possibilities!

## Slide 3: Class notes and code
All the class notes and code can be downloaded from GitHub:
  https://github.com/RochesterMakerSpace/ArduinoClass
Pull down the green “Code” button and select “Download ZIP”

## Slide 4: Computers, Microcontrollers, Arduino
Conventional computers can be described by 5 main components:
  CPU – the Central Processing Unit executes instructions
  Program memory – the instructions
  Data memory – the data
  I/O interfaces and devices – connecting disks, screens, keyboards, mice, etc.
  Software - Operating system, utility programs, applications
Microcontrollers are a computers on a chip typically including a CPU, and program and data memory with connectors for General Purpose Input and Output (GPIO).
Arduino is an open-source board design, originally designed in 2006, that is combined with a free, basic development environment

## Slide 5: Microcontrollers  Computer systems

## Slide 6: Arduino Uno R3
The canonical Arduino design
Focus is on experimentation and learning
A simple, low-cost, small computer
Genuine: $22, Clone: $11
Modest processing power (16 Mhz)
Small space for code (32KB)
Small space for data (2KB)
Wide range of GPIO connectivity options for devices or circuits
Easy USB connection and good, free software development environment
Huge community of ‘makers’ providing videos, tutorials, examples, projects, devices, advice

## Slide 7: Many Arduino variants
Faster processor
Bigger programs
More data
More pins to connect devices
More portable
Different form factor

## Slide 8: New Arduino Nanos
Arduino Nano Every $11.90
ATMega4809 20 Mhz
48 KB Flash, 6 KB RAM
Arduino Nano 33 IoT $18.40
SAMD21, 32-bit, 48 Mhz
256 KB Flash, 32 KB RAM
WiFi, Bluetooth, BLE, 6 Axis IMU
Arduino Nano 33 BLE $20.20
nRF52840, 32-bit, 64 Mhz
1 MB Flash, 256 KB RAM
Bluetooth, BLE, 9 Axis IMU
Arduino Nano 33 Sense $31.10
nRF52840, 32-bit, 64 Mhz
1 MB Flash, 256 KB RAM
Bluetooth, BLE, 9 Axis IMU
Humitity, Temp, Pressure, Mic, gesture ,proximity, light sensors
Arduino Nano Every
Arduino Nano 33 IoT
Arduino Nano 33 BLE
Arduino Nano 33 Sense

## Slide 9: Arduino GPIO
Simple direct connection for digital input and output
Simple direct connection for analog input
Onboard pulse width modulation (PWM)
4 ways to connect to other chips:
GPIO – Digital I/O or Analog Input
I2C – Inter-Integrated-Circuit
SPI – Serial Peripheral Interface
Serial – asynchronous serial

## Slide 10: I2C
I²C ( Inter-Integrated Circuit ), pronounced I-squared-C , is a synchronous , multi-master, multi-slave , packet switched , single-ended , serial computer bus invented in 1982 by Philips Semiconductor (now NXP Semiconductors ). It is widely used for attaching lower-speed peripheral ICs to processors and microcontrollers in short-distance, intra-board communication. Alternatively I²C is spelled I2C (pronounced I-two-C) or IIC (pronounced I-I-C).
Wikipedia

## Slide 11: SPI
The Serial Peripheral Interface (SPI) is a synchronous serial communication interface specification used for short distance communication, primarily in embedded systems. The interface was developed by Motorola in the mid 1980s and has become a de facto standard. Typical applications include Secure Digital cards and liquid crystal displays.
    Wikipedia

## Slide 12: Arduino Integrated Development Environment (IDE)
Free download from https://www.arduino.cc/en/Main/Software
Simple, fixed program structure
Uses a programming language that is a simplified variant of c++
Support for other processors, ESP8266, STM32, Pi Pico, etc.
Alternatives:
Arduino IDE 2.0
Platform IO (VS Code/Atom)

## Slide 13: Arduino Integrated Development Environment (IDE)
Change board type
Arduino UNO or Arduino UNO clone
  Tools|Board|Arduino AVR Boards|Arduino\Genuine UNO
Arduino Leonardo or Arduino Leonardo clone (Velleman – white board)
  Tools|Board|Arduino AVR Boards|Arduino Leonardo

## Slide 14: Sketches and Circuits
Blink (File|Examples|01.Basics|Blink)
Focus: basic code of a sketch
Experiment: change the rate of blinking
Can use Built In LED connected to pin 13 instead of external LED

## Slide 15: LED Polarity

## Slide 16: Sketches and Circuits
Button (File|Examples|01.Digital|Button)
Focus: breadboarding, variables
Experiment: reverse the effect of a button press
Can use Built In LED connected to pin 13

## Slide 17: Sketches and Circuits
Fade (File|Examples|01.Basics|Fade)
Focus: PWM
Experiment: change the variables

## Slide 18: Fade LED PWM

## Slide 19: Sketches and Circuits
ReadAnalogVoltage (File|Examples|01.Basics|ReadAnalogVoltage)
Focus: analog input, monitor/plotter
Experiment: convert to use the 3.3v pin
Use function to convert sensor value to voltage:
float SensorToVoltage(int sensor)
{
return sensor * (5.0/1023.0);
}

## Slide 20: Sketches and Circuits
Sweep (File|Examples|Servo|Swee[)
Focus: #includes, motor control
Experiment: restrict the servo range of motion

## Slide 21: Servo PWM

## Slide 22: Sketches and Circuits
BlinkWithoutDelay (File|Examples|02.Digital|BlinkWithoutDelay)
Focus: code execution timing
Experiment: print to the serial monitor at the same time
Can use Built In LED connected to pin 13 instead of external LED

## Slide 23: Sketches and Circuits
Debounce (File|Examples|02.Digital|Debounce)
Focus: the mechanical world
Experiment: how short can your delay be without flickering the led?
Can use Built In LED connected to pin 13 instead of external LED

## Slide 24: Resources
https://www.instructables.com/id/Arduino-Projects/ A great source of inspiration Shows many cool projects you can accomplish with an Arduino
Introduction to Arduino: A piece of cake! Alan G. Smith (alan@introtoarduino.com) Hardcopy available at http://www.amazon.com The most recent PDF is free at http://www.introtoarduino.com
https://www.arduino.cc The official web site for Arduino Tutorials, documentation, example projects, shop
https://www.adafruit.com A DIY site loaded with Arduino and Raspberry Pi products Tutorials, step-by-step instructions, example projects, shop
https://www.sparkfun.com/ An electronics retailer with lots of Arduino and Raspberry Pi products
https://www.pololu.com/ An online retailer with lots of robotics components
https://www.seeedstudio.com/ An online retailer of project components
https:// blog.tinkercad.com/official-guide-to-tinkercad-circuits / Cloud-based 3D CAD and Circuit design tool

## Slide 25: Nightlight example
Night Light – a simple circuit to switch on an LED when it gets dark
  Open|Maker/Documents/ArduinoClass/nightlight/nightlight.ino
  Demonstrates use of analog input and digital output
  Demo: https://www.youtube.com/watch?v=2GqKbUyhUww

## Slide 26: Nightlight example - Breadboard

## Slide 27: Nightlight example - Schematic