## Slide 1: Introduction to Arduino
Rochester MakerSpace
2019
Notes: Welcome
Introductions

## Slide 2: Class Objectives
Become familiar with Arduino hardware and software
Be aware of the range of Arduino-supported boards and how to choose one for your project
Understand how to connect and operate Arduino hardware from a PC or Mac
Understand how to create and run a program on an Arduino
Understand how to control a simple circuit from an Arduino
Get a starter list of resources for learning more
Be excited by the possibilities!

## Slide 3: Computers, Microcontrollers, Arduino
Conventional computers can be described by 5 main components:
  CPU – the Central Processing Unit executes instructions
  Program memory – the instructions
  Data memory – the data
  I/O interfaces and devices – connecting disks, screens, keyboards, mice, etc.
  Software - Operating system, utility programs, applications
Microcontrollers are a computers on a chip typically including a CPU, and program and data memory with connectors for General Purpose Input and Output (GPIO).
Arduino is an open-source board design, originally designed in 2006, that is combined with a free, basic development environment

## Slide 4: Microcontrollers  Computer systems

## Slide 5: Arduino Uno R3
The canonical Arduino design
Focus is on experimentation and learning
Simple, low-cost, small computer
Modest processing power
Small space for code
Small space for data
Wide range of GPIO connectivity options for devices or circuits
Easy USB connection and good, free software development environment
Huge community of ‘makers’ providing videos, tutorials, examples, projects, devices, advice

## Slide 6: Arduino Integrated Development Environment
Free download from https://www.arduino.cc/en/Main/Software
Simple, fixed program structure
Uses a programming language that is a simplified variant of c++

## Slide 7: Many Arduino variants
Faster processor
Bigger programs
More data
More pins to connect devices
More portable
Different form factor

## Slide 8: Arduino GPIO
Simple direct connection for digital input and output
Simple direct connection for analog input
Onboard pulse width modulation (PWM)
3 ways to connect to other chips:
I2C – Inter-Integrated-Circuit
SPI – Serial Peripheral Interface
Serial – asynchronous serial

## Slide 9: I2C
I²C ( Inter-Integrated Circuit ), pronounced I-squared-C , is a synchronous , multi-master, multi-slave , packet switched , single-ended , serial computer bus invented in 1982 by Philips Semiconductor (now NXP Semiconductors ). It is widely used for attaching lower-speed peripheral ICs to processors and microcontrollers in short-distance, intra-board communication. Alternatively I²C is spelled I2C (pronounced I-two-C) or IIC (pronounced I-I-C).
Wikipedia

## Slide 10: SPI
The Serial Peripheral Interface (SPI) is a synchronous serial communication interface specification used for short distance communication, primarily in embedded systems. The interface was developed by Motorola in the mid 1980s and has become a de facto standard. Typical applications include Secure Digital cards and liquid crystal displays.
    Wikipedia

## Slide 12: Resources
https://www.instructables.com/id/Arduino-Projects/ A great source of inspiration Shows many cool projects you can accomplish with an Arduino
Introduction to Arduino: A piece of cake! Alan G. Smith (alan@introtoarduino.com) Hardcopy available at http://www.amazon.com The most recent PDF is free at http://www.introtoarduino.com
https://www.arduino.cc The official web site for Arduino Tutorials, documentation, example projects, shop
https://www.adafruit.com A DIY site loaded with Arduino and Raspberry Pi products Tutorials, step-by-step instructions, example projects, shop
https://www.sparkfun.com/ An electronics retailer with lots of Arduino and Raspberry Pi products
https://www.pololu.com/ An online retailer with lots of robotics components
https://www.youtube.com/ Countless tutorial videos and example projects

## Slide 13: Getting started hands-on
Night Light – a simple circuit to switch on an LED when it gets dark
  Demonstrates use of analog input and digital output
PWM (https://www.youtube.com/watch?v=Y1QraI5i_XM)